## Slide 1
HACKATHON BUILD
01
Recognize.
Sort.
Connect.
A mobile trash-sorting rover
with local vision and a shared dashboard.
Notes: Project overview. Sources: README.md; docs/hardware.md; docs/architecture.md. Hardware photograph: Media/IMG_3596.jpg. Photo preserves the actual prototype.

## Slide 2
The software and hardware
HACKATHON BUILD
02
LAPTOP
Flask serves the dashboard.
CLIP runs inference on the laptop.
TWO RASPBERRY PIS
One relays drive commands.
The other streams the camera and moves lids.
ARDUINO + CNC SHIELD
USB serial reaches the motor controller.
Four steppers drive the mecanum wheels.
Notes: Sources: docs/architecture.md, especially Two Pis in practice; docs/hardware.md; web_server.py; BRH_Test/rover_bridge.py; BRH_Test/driveController/driveController.ino. The laptop hosts Flask and CLIP. Separate Pi processes handle drive and camera/lids. TigerData is a remote PostgreSQL service. Hardware photo: Media/IMG_3597.jpg.

## Slide 3
Local CLIP recognition
HACKATHON BUILD
03
The laptop compares camera
frames with text labels.
CLIP ViT-L/14
RECYCLING
Bottle and cardboard
TRASH
Paper towel and chip bag
Three readings over at least 0.5 seconds
produce a stable item lock.
Other labels return no supported item. Match scores compare candidates.
Notes: Sources: classifier.py MODEL_ID, TARGETS, Classifier.predict; classifier_service.py ItemLock.READINGS and LOCK_SECONDS. Default model is openai/clip-vit-large-patch14. The model compares the whole frame with text candidates, including non-target labels. Only four item families are reported. Three or more readings spanning at least 0.5 seconds form a lock. Relative scores are candidate comparisons, not accuracy probabilities. Screenshot: source recording at 167.5 seconds, actual bottle and recycling result.

## Slide 4
A detection opens the matching lid
HACKATHON BUILD
04
LIVE ITEM LOCK
The laptop sends the bin command
over Wi-Fi UDP to the lid Pi.
CALIBRATED SERVO LIDS
The Pi drives the PCA9685 over I²C.
Each bin has its own servo channel.
AUTOMATIC CLOSE
The lid stays open for about 5 seconds
after the last matching reading.
Automatic lids use live scans when enabled. Photo uploads do not open lids.
Notes: Sources: classifier_service.py Service.track; lid.py RemoteLid and Lid; lid_server.py; docs/hardware.md. Live locked readings trigger open Trash or open Recyclable through UDP 5006. The lid Pi controls PCA9685 over I2C, channel 0 trash and channel 3 recycling. HOLD_SECONDS=5 after the last reading. Lid automation must be enabled. Photos do not open lids. Image: Media/IMG_3595.jpg.

## Slide 5
Website, voice and hand controls
HACKATHON BUILD
05
WEBSITE CONTROLS
Direction buttons and throttle
send commands through the rover bridge.
GROK VOICE
Spoken directions call a drive tool.
The bridge sends the motor command.
MEDIAPIPE HAND TRACKING
Wrist-to-fingertip angle sets direction.
Bluetooth carries the angle to the rover.
One driving browser at a time. A missing heartbeat stops the rover after 1.5 seconds.
Notes: Sources: BRH_Test/rover_bridge.py set_mode, _camera_loop, _watchdog; BRH_Test/voice_control.py DRIVE_TOOL and DIRECTION_TO_CMD; docs/hardware.md. Website directions support keyboard, touch/mouse. Grok voice uses xAI realtime WebSocket and invokes drive_rover. MediaPipe runs locally; wrist-to-index-tip angle is rounded to five degrees and sent over Bluetooth. Wi-Fi receiver supports WASD, not angles. One driving session at a time. Heartbeat loss beyond 1.5 seconds stops/releases rover. Hand image: Media/HandGuestureProof.png.

## Slide 6
Every detection has a record
HACKATHON BUILD
06
TigerData PostgreSQL
Computers and phones access the same history
through the dashboard.
One scan ID prevents repeat frames from creating duplicate records.
The ledger stores metadata, not camera images. Lid openings record collection events.
Notes: Sources: BRH_Test/database.py initialize, add_detection, add_collection, bin_contents, empty_bin; dashboard_classifier.py log_detection and auto_recorded; docs/architecture.md Logging and points. Each locked live scan and each photo records item, bin, score, source, time. Unique scan_id avoids duplicate rows as frames repeat. With configured DATABASE_URL the backend uses TigerData PostgreSQL, otherwise SQLite. Lids opening auto-records one collection event per locked scan. The camera does not verify a physical deposit. Photos and disabled lids require manual confirmation. No images stored in the ledger. Screenshot: output/video/assets/live-log-site.png. README.md manual-confirmation wording is older than the current automatic collection implementation.

## Slide 7
Gemini guidance for unfamiliar items
HACKATHON BUILD
07
Upload a photo or ask about
an unfamiliar item.
Material guidance
Preparation steps
Reuse ideas
Advice stays separate from local CLIP
recognition and rover control.
Gemini processes submitted content in the cloud. The guide does not record drops.
Notes: Sources: BRH_Test/GEMINI.md; BRH_Test/gemini_guide.py; web/gemini.js. Guide accepts question, optional location and selected photo. Photos are decoded, resized and stripped of EXIF. Submitted content goes to Google Gemini. It is a separate advisory flow with no drive, lid or ledger tools and no live municipal-rule lookup. Screenshot: Media/Gemini-Integration.png.